## Slide 1: Matlab modelling

## Slide 2: Content
Directory 설명
각 directory별 file들 설명
  Analysis
  Receiver
  Transmitter
  Common
GUI 설명
Function hierarchy
  Receiver
  Transmitter

## Slide 3: directory 구조

## Slide 4: Analysis
File name | Description
BER2Q.m | BER to Q
CSFigure.m | Constellation
EbNo2SNR.m | EbNo 2 SNR for OFDM
EsNo2EbNo.m | EsNo 2 EbNo for OFDM
FrameAnalysis.m | Analysis for each frame
OFD.m | Spectrum
OTD.m | Power in time domain
SNR2EbNo.m | SNR 2 EbNo for OFDM
cfo_calc.m | CFO estimation from DC interval
idealBER_EBNO.m | Ideal BER as a function of EbNo for OFDM
osnr2snr.m | OSNR to SNR
snr2osnr.m | SNR to OSNR

## Slide 5: Common
File name | description
AutoCorr.m | Auto correlation
CrossCorr.m | Cross correlation
Get_int.m | CRT
NLowPassFilter.m | Low pass filter
NLowPassFilter1.m | Low pass filter

## Slide 6: Receiver files
File name | Description
NRx1Frame.m | 1 frame receiver ( Specific for off-line experiment )
RxMain.m | 1 frame receiver
OFDE.m | OFDE for CD compensation
SPMPostComp.m | SPM compensation for nonlinear
NRxAGC.m | Automatic Gain control
NRxFindCS_MIMO_energy.m | Frame symbol synchronization ( only for simulation )
NRxSCFOcor.m | CFO estimation and compensation
NRxFindSync.m | Symbol synchronization
NRxChannelEst.m | Channel estimation
ISFA.m | ISFA
FFTnComp.m | Data symbol( Channel equalization, CPE estimation )
NRxDemapper.m | Demapper

## Slide 7: Transmitter files
File name | Description
TxMain.m | TX main
IFFTnAddCP_PreComp.m | IFFT
NCalDelay_ver2.m | Delay calculation for subband ( band division )
NMapper.m | Mapper
NPilot.m | Pilot subcarrier add
NPrecompCD.m | Precompensation
Preamble_PreComp.m | Insert training symbols

## Slide 8: GUI

## Slide 9: GUI 1
Carrier frequency offset compensation
Homodyne ( disable시 DC interval을 이용하여 given CFO estimation)
Common phase error( phase rotation) compensation
Symbol synchronization ( to find the start of symbol)
Frame synchronization ( to find the start of frame )
Carrier frequency offset estimation type
Single frequency CFO based on CRT ( two training symbols)
Conventional CFO based on CRT ( two training symbols)
EEO (Combined with Zhou’s algorithm)
Zhou’s algorithm
Single frequency CFO based on CRT ( one training symbol)
Decision feedback phase rotation
MIMO emulation (1: MIMO, 0: SISO)
Extend subcarriers to apply ISFA to edge subcarriers
Input channel selection ( 1:CH1, CH3, 0:CH2, CH4)

## Slide 10: GUI II
Channel estimation (zero forcing)
ISFA disable
ISFA enable
  with ISFA size(amplitude) of
  and ISFA1 size(I,Q separate) of
Sampling offset selection (Obsolete)
Sampling offset 0
Sampling offset 1
Sampling offset 2
Sampling offset 3
Interpolation
Overampling
Symbol synchronization point
QAM : 24 QAM
The sampling rate of transmitted signal (GHz)
The sampling rate of incoming signal (GHz)
Low pass filter cut off frequency (GHz)
Sweep ISFA size to find the
optimum ISFA size
  ISFA from 0 to
  and ISFA1 size from 0 to
Sweep the sampling offset
Sweep the syncpoint from 0 to
Fiber length
Launch power(?):
Enable self phase modulation (SPM) post compensation
OFDE enable

## Slide 11: GUI III
File read (C1, C2, C3, C4로 시작하거나, I.xxx, Q.xxx로 된 파일set이어야 함.)
Oscilloscope data is interpolated using time information of triggered data
File read시 CH1, CH2를 negative로 read함
읽은 파일 이름 display
Oscilloscope를 trigger하고 data읽어옴.
Initialize
OFDM parameters (InitOFDM_xxx.m)
BER related parameters
Frame decoding (NRx1Frame.m 을 실행시킴)
Save the current data in file (C1xxx, C2xx, C3xxx, C4xxx)
20개의 frame을 decoding할 때까지
진행,
한 frame의 error개수가 100개가 넘어가면 stop함.

## Slide 12: GUI IV
BER ( X pol, Y pol )
The estimated CPE ( one frame)
Mean square estimation error of CFO
Mean SNR
The total number of bit errors
(X pol, Y pol)
The total number of bits
The total number of frames
Spectrum of input signal
Constellation
Time domain signal
Display OFDM parameters
Display graphic data
Accumulated bit errors as a function of subcarrier (X pol)
Accumulated bit errors as a function of subcarrier (Y pol)
Frame별 bit error개수의 추이
EVM vs symbol ( one frame)

## Slide 13: Hierarchy of receiver
NRx1Frame.m |  |  | 
 | RxMain.m |  | 
 |  | OFDE.m | 
 |  | SPMPostComp.m | 
 |  | NRxAGC.m | 
 |  | NRxFindCS_MIMO_energy.m | 
 |  | NRxSCFOcor.m | 
 |  | NRxFindSync.m | 
 |  | NRxChannelEst.m | 
 |  |  | CalcH2.m
 |  | ISFA.m | 
 |  | FFTnComp.m | 
 |  |  | FFTnRemoveCP.m
 |  | NRxDemapper.m | 
 |  |  | NRxDemapper_sc.m
 |  |  | NRxDemapper_simple.m

## Slide 14: Hierarchy of transmitter
run_gen_AWG.m |  |  | 
 | InitOFDM_06Oct.m |  | 
 | ReInitOFDM.m |  | 
 | NCalDelay_ver2.m |  | 
 | GenStim.m |  | 
 | TxMain.m |  | 
 |  | NMapper.m | 
 |  |  | NMapper_sc.m
 |  |  | NMapper_simple.m
 |  | NPilot.m | 
 |  | IFFTnAddCP_PreComp.m | 
 |  |  | ifft_band.m
 |  | NPrecompCD.m | 
 |  |  | NPrecompCD_ver1.m
 |  |  | NPrecompCD_ver2.m
 |  |  | NPrecompCD_ver3.m
 |  |  | NPrecompCD_ver4.m
 | gennerate_AWG.m |  |